## Slide 1
TX Huffman Tree to Code Length
TX builds a Huffman tree by repeatedly merging the two lowest-weight nodes, then uses leaf depth as code_len.
1. Initial partial trees
Start with one leaf per symbol
2
Z
7
K
24
M
32
C
37
U
42
D
42
L
120
E
Priority queue rule
Merge two lowest weights.
Parent weight = sum.
parent = w1 + w2
2. Merge until root
Each row is one merge:
1
Z2 + K7
9
2
9 + M24
33
3
C32 + 33
65
4
U37 + D42
79
5
L42 + 65
107
6
79 + 107
186
7
E120 + 186
306
Stop: one root = 306
3. Final tree and code_len
d0
d1
d2
d3
d4
d5
d6
306
186
79
107
65
33
9
120
E
len=1
37
U
len=3
42
D
len=3
42
L
len=3
32
C
len=4
24
M
len=5
2
Z
len=6
7
K
len=6
code_len = leaf depth: E=1, U/D/L=3, C=4, M=5, Z/K=6
TX output from this stage is code_len for each symbol; the tree shape itself is not stored in the compressed block.

## Slide 2
TX Canonical Huffman Encoding
Tree depth gives code_len. TX sorts symbols and assigns deterministic canonical codes.
1. Read tree depth
code_len = tree depth
symbol depth len
E 1 1
U 3 3
D 3 3
L 3 3
C 4 4
M 5 5
Z 6 6
K 6 6
code_len
2. Sort
Canonical order:
shorter code_len first
same length: ASCII first
Order
E
D
L
U
C
M
K
Z
len=3: D < L < U
3. Assign code
Start: current_code = 0
len
assigned code
1
E = 0
2
no symbol; shift left
3
D = 100
L = 101
U = 110
4
C = 1110
5
M = 11110
6
K = 111110
Z = 111111
4. TX tables
Header: codebook info
E:1 D:3 L:3 U:3
C:4 M:5 K:6 Z:6
Payload: canonical codes
E = 0
D = 100
L = 101
U = 110
C = 1110
M = 11110
K = 111110
Z = 111111
TX output: header carries codebook information; payload carries compressed bits encoded with canonical codes.

## Slide 3
RX Canonical Huffman Reconstruction
RX reads only symbol + code length from the header, then rebuilds the same canonical code table as TX.
1. Read header entries
Header carries codebook
information:
symbol code_len
E 1
D 3
L 3
U 3
C 4
M 5
K 6
Z 6
No original tree stored
2. Sort entries
Canonical order:
shorter code_len first
same length: ASCII first
Order
E
D
L
U
C
M
K
Z
len=3: D < L < U
3. Recreate codes
Start with current_code = 0.
len
generated code
1
E = 0
2
no symbol, shift left
3
D = 100
L = 101
U = 110
4
C = 1110
5
M = 11110
6
K = 111110
Z = 111111
4. RX lookup table
The decoder stores prefix rules:
code symbol
0 E
100 D
101 L
110 U
1110 C
11110 M
111110 K
111111 Z
Same table as TX because the canonical rule is deterministic.
Key idea: RX reconstructs the codebook from code_len; it does not transmit or rebuild the original Huffman tree.

## Slide 4
RX Huffman Payload Decoding
After the table is rebuilt, payload bits are consumed by prefix match until block_size output bytes are recovered.
Compressed block seen by RX
mode
2b
block_size
7 bytes
symbol_count
8 entries
entries
E:1 D:3 L:3 U:3 ...
payload bits
0 0 0 100 100 101 0
Header = dictionary information. Payload = actual compressed data encoded using that dictionary.
1. Match prefix
Input window:
1001010...
first match: 100 = D
Consume 3 bits, then continue with the next prefix.
2. Decode sequentially
Example payload segmentation:
0
E
0
E
0
E
100
D
100
D
101
L
0
E
Repeated symbols come from repeated codewords in the payload, not from per-symbol counts in the header.
3. Stop by block_size
Recovered bytes:
E E E D D L E
output_count = 7
block_size = 7
DONE
Key idea: the payload carries the repeated occurrences; block_size tells RX when the original block is fully recovered.